## Slide 1
Wind Farm Project Development, WiSe 2024/25
Team 3: Wind Farm Project in Gujarat, India
Presented by: Matriculation No.
Mozafary Mostafa 750247
Patil Rahul 750532
Soni Karan 760153
Guided by: Dr. Marina Blohm
Date : 15.01.2025
Place: Flensburg

## Slide 2: Overview
Overview of wind farm development in Gujarat
Guidelines and Regulations
Project development timeline
Wind Area selection
Grid infrastructure and cable routing
Strategies community engagement
Land Leasing
Addressing conflicting
10. Logistics and Transformation
11. Profitability Analysis
12. Results
13. Long Term Strategy
14. Barriers and Obstacles
15. Conclusion
16. References

## Slide 3: Agenda
Introduction
Guidelines and Regulations
Wind Farm Development
Environmental impact and Conflicts
Land Leasing
Transportation
Economic Analysis
Future Strategies

## Slide 4: 1. Introduction
India:
India ranks fourth in terms of installed wind power capacity
High Wind potential 132 GW with minimum 32% CUF
Ambitious Target(Wind) : 140 GW by 2030 (48 GW Current)
Energy Security

## Slide 5: 1. Introduction
Gujarat:
As May 2024, makes it the leading state in India for wind energy.
12.2 GW installed wind power capacity (26% Of total capacity)
Second rank, Tamil Nadu 11 GW
Why?
Geographic advantages
Government supports
Land policy
Tax benefits(First 10 Years no taxes).

## Slide 6: 3. Approval Bodies
Gov.
Body
Ministry of New and Renewables (MNRE)
Central Agencies
National Institute of Wind Energy(NIWE)
State
Agencies
Gujarat Energy Development Agency(GEDA)
Ministry for Environment, forest and Climate change(MoEFCC)
Ministry of Defence (MoD)
Directorate General of Civil Aviation
Gujarat Power Corporation Limited (GPCL)
Gujarat Pollution Control Board(GPCB)
Revenue Department and Local Panchayat

## Slide 7: 4. Permits and Approvals
Consent to Establish from GSPCB
NOC from State Electricity board
Land Allotment letter
NOC from DLIR Department
Permission for Forest Department
NOC from Mining Department
NOC from AAI and MoD
Power Purchase Agreement
NOC from Village Panchayat

## Slide 8: 5. Micro siting Guidelines
Criteria | Buffer Distance
Micro siting within Wind Farm | 2D-3D
Public Roads, railway tracks, highways, buildings, public institutions | HH+0.5∙RD+5m
Eco-Sensitives Zones | 10 KM
Forest | 6.6 M from Ground (Power Lines)
Satic Air Defence Radar | 10 KM
Airports and Airstrips | 20 KM
Rivers | 250 M

## Slide 9: 6. Wind Farm development
Identification of Potential Site
Pre-Feasibility Study
Grid Connectivity
Land Acquisition and Approvals
Environmental and Social Impact Assessment
Financial Planning
Wind Farm Development

## Slide 10: 6. Wind Farm development
Identification of Potential Sites (QGIS)
Analyse Wind site:
Wind speed data at 100m height
Coordinate Reference System: WGS 84/ UTM zone 43N, Authority ID: EPSG:32643
Integrated wind speed data onto the white map layer [Use the clip Raster by Mask Layer Tool]
GIS Layers | Distances [m]
Buildings | 250
Forests | 10,000
Military Areas | 10,000
Railways/ Industrial | 250
Roads | 250
Airports/ Airfields | 20,000
Rivers | 250

## Slide 11: 6. Wind Farm development
Pre-Feasibility study
Criteria For site selection
Wind Resource Availability
Topography and Terrain
Land Availability
Grid Infrastructure
Environmental considerations
Soil Conditions
Logistics

## Slide 12: 6. Wind Farm development
Selection of site

## Slide 13: 4. Wind Area Selection
Used Google Earth Pro for a comprehensive site assessment

## Slide 14: 4. Wind Area Selection
Type of Land and Soil Condition
Soil :- Residual Sandy soil with reddish brown in color
Land :- Private farmland (100X100 m)

## Slide 15: 4. Wind Area Selection
Elevation Profile of Site

## Slide 16: 4. Wind Area Selection
Six Suzlon 2.1 MW wind turbines, strategically positioning them to account for wind direction
Predominant Wind direction of Site

## Slide 17: 4. Wind Area Selection
Wind Farm Capacity :- 12.6 MW
Turbine:- S97*2100(112 m HH)
Why Suzlon?
Local Manufacturer
High-capacity utilization factor (CUF)
Low Cost Availability
Logistics
Selection of WTGs

## Slide 18: 5. Grid Infrastructure and Cable Routing
Our wind farm has a capacity of 12.6 MW, which is relatively below 20 MW. Therefore, we utilized an available substation.
The substation, named Renew Wind Energy (AP2) Pvt Ltd, operates at 33/220 kV.
The length of the 33 kV line from the inside wind farm is 4.41 Km and from wind farm area to the pooling substation is 16 km.
Followed existing roads for transmission line in order to avoid conflicts and permissions.

## Slide 19: 7. Strategies of Community Engagement
Benefits of the Wind Park Project
Job Creation:
  1 full-time site manager
  2 full-time operators for maintenance and repairs
Profit for Landowners
Addressing Power Outages:
  A reliable electricity supply for the village (currently interruptions caused by infrastructure issues, scheduled cuts, or weather conditions.)
Infrastructure Development:
  Supports the expansion of rural infrastructure
31th July 2012, the world's biggest blackout [source:nbcnews]

## Slide 20: 7. Strategies of Community Engagement
Community Meeting
Engage Local Leaders
Transparency
Benefit Sharing
Regular Updates
Community Feedback
Raise Awareness
Long Term Engagement
Community Meetings: Highlight benefits (jobs, infrastructure, clean energy) and address concerns.
Engage Local Leaders: Gain trust and support from key influencers.
Transparency: Share project details, timelines, and impacts openly.
Benefit Sharing: Provide scholarships, infrastructure upgrades, or community funds.
Regular Updates: Keep everyone informed on progress through consistent communication.

## Slide 21: 8. Land Leasing
Land Leasing Overview:
Secure land for wind park projects under Gujarat’s progressive renewable energy policies.
Lease Duration: 40 years for government fallow land.
Policy Scope: Focus on renewable energy generation to support Gujarat’s industrial and green energy goals.
Eligibility: Companies with experience in renewable energy and sufficient financial capacity.

## Slide 22: 8. Land Leasing
Eligibility and Allocation:
Eligibility:
Minimum 500 MW renewable energy generation experience.
Net worth: ₹1200 crore/lakh metric tons of energy/year.
Industries requiring 1 lakh metric tons/year of green hydrogen prioritized.
Land Allocation:
Exclusive use for wind energy projects.
Cap of 30 lakh metric tons/year green hydrogen production per entity.
Reserved land for future state requirements.

## Slide 23: 8. Land Leasing
Application and Approval Process:
Application Submission:
Preliminary preparation report (technical and financial).
Verification:
Nodal Agency (GPCL) validates eligibility and technical aspects.
Review & Recommendation:
High Power Committee (HPC) evaluates proposals.
Final Approval:
Government decision via Revenue Department.
Lease agreement executed with a tripartite agreement.

## Slide 24: 8. Land Leasing
Responsibilities & Compliance:
Developer Responsibilities:
Infrastructure: Roads, transmission, and water systems.
Financial: ₹180,000 (€ 2050)/ha annual rent (15% increase every 3 years).
Progress Milestones:
  50% capacity in 3 years.
  100% capacity in 8 years.
Compliance:
Periodic reviews to ensure milestones.
Unused land subject to reclamation.

## Slide 25: 8. Land Leasing
Number of owner | Area ( ) | Financial by rule (1/year) | Bonus (1/year) | Total (per year)
1 (WT) |  | € 2050 | € 921 | € 2971
2 (WT) |  | € 2050 | € 921 | € 2971
3 (WT) |  | € 2050 | € 921 | € 2971
4 (WT) |  | € 2050 | € 921 | € 2971
5 (WT) |  | € 2050 | € 921 | € 2971
6 (WT) |  | € 2050 | € 921 | € 2971
7 (transmission line) |  | € 4100 | € 921 | € 2971
Number of owner |  | Financial by rule (1/year) | Bonus (1/year) | Total (per year)
1 (WT) |  | € 2050 | € 921 | € 2971
2 (WT) |  | € 2050 | € 921 | € 2971
3 (WT) |  | € 2050 | € 921 | € 2971
4 (WT) |  | € 2050 | € 921 | € 2971
5 (WT) |  | € 2050 | € 921 | € 2971
6 (WT) |  | € 2050 | € 921 | € 2971
7 (transmission line) |  | € 4100 | € 921 | € 2971
Table xx: Land leasing own strategy [own]
Bonus
Land Leasing own strategy
Figure xx: Information of land owner [own]

## Slide 26: 9. Addressing Conflicting Interests
Environmental Conflicts in Wind Energy Projects
Land Use Challenges:
Competition over agricultural, forest, and community lands.
Protected areas like the Western Ghats face ecological damage.
Biodiversity Impact:
Bird and bat fatalities due to turbine collisions.
Habitat destruction from road construction and deforestation.
Environmental Trade-offs:
Noise pollution and shadow flicker disturb local communities.
Changes in local hydrology and microclimates from large-scale projects.

## Slide 27: 9. Addressing Conflicting Interests
Socio-Economic and Governance Conflicts:
Community Livelihood Loss:
Displacement from common lands and inadequate compensation.
Encroachment on tribal lands and loss of natural resources.
Regulatory Gaps:
Lack of stringent Environmental Impact Assessments (EIA).
Unplanned projects ignore landscape-scale implications.
Competing Priorities:
Conflict between energy development and agricultural or tourism needs.
Balancing renewable energy goals with environmental preservation.

## Slide 28: 10. Logistics and Transformation
NH48
NH4
NE1
NH64
NH27
754k
1
2
3
4
Wind Turbine Manufacturing components | Manufacturing Locations | Distance between Manufacturing location to Wind farm [km]
Nacelle | Daman, Gujarat, India | 743
Nacelle Cover | Daman, Gujarat, India | 743
Hub | Daman, Gujarat, India | 743
Rotor Blades | Bhuj, Gujarat, India | 57
Tower | Gandhidham, Gujarat, India | 136
Electrical | Vadodara, India | 544
Location: Poladia, Gujarat, India
Why Suzlon company wind turbine?
Manufacturing in Gujarat
Government provides incentives (Made in India)

## Slide 29: 10. Logistics and Transformation
Distance Between State highway to Wind Farm: 25 km

## Slide 30: 11. Profitability Analysis
Input Parameters of Annual Energy For Wind Farm:
Figure xx: Wind pro report [own]
Figure xx: Wind pro report [own]

## Slide 31: 11. Profitability Analysis
Input Parameters to calculate Profit analysis calculation:
Parameter | Economics | Unit
Number of WT | 6 | -
Installation output | 2100 | KW
Total output | 12600 | kW
Gross Energy Yield | 39924500 | KWh/a
Total losses | 2.20 | %
Net Energy Yield | 399,046,161 | kWh
Site Quality | 71.04 | %
Feed in Tariff | 0.033 | Euro/kWh
Total Investment Costs | 98,07,253 | Euro
Total Operating Costs | 1,05,000 | Euro
Constant Payment Loan Type (Debt ratio) | 72.73 | %
Equity | 26,74,327 | Euro
Term | 17 | Years
Interest rate of Bank | 9.0 | %
Debt Capital | 71,32,926 | Euro
Inflation rate | 5.16 | %
Table xx: Input parameters for calculating profit analysis [own]
Take data from WindPro Calculation
INR 3 per kwh
Capital costs:
1 MW = INR 70 million (Euro 0.791 million)
Operating costs:
1 MW = INR 0.75 million/year = (Euro 0.105 million)
Last 10 years average

## Slide 32: 11. Profitability Analysis
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044
Income | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158
Figure xx: Income Vs Years [own]
Income vs Years:
Income: 1.29 Million/ year
operation period: 20 years

## Slide 33: 11. Profitability Analysis
Chart: Operating costs
Chart: 
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Betriebskosten | 260419.05 | 266117.7772 | 272110.6157 | 128412.7445 | 135040.1263 | 142009.5472 | 149338.6599 | 157046.0282 | 165151.1737 | 173674.6257 | 182637.9732 | 192063.919 | 201976.3378 | 212400.3366 | 223362.318 | 234890.0472 | 247012.7226 | 259761.0492 | 273167.3169 | 287265.4822
Figure xx: Operating cost Vs Years [own]
Operating costs vs Years:
Operating costs: 0.25 Million staring year
operation period: 20 years

## Slide 34: 11. Profitability Analysis
Chart: 
| Eigenkapital | Fremdkapital
 | 0.2727 | 0.7273
Chart: Duration in years
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Repayment | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581
Interest | 641963.3029 | 641963.3029 | 641963.3029 | 623082.0293 | 585319.4821 | 547556.9349 | 509794.3876 | 472031.8404 | 434269.2932 | 396506.7459 | 358744.1987 | 320981.6515 | 283219.1042 | 245456.557 | 207694.0098 | 169931.4625 | 132168.9153 | 94406.3681 | 56643.8208 | 18881.2736
Figure xx: Investment [own]
Figure xx: Debt service Vs years [own]
Debt service Vs Years:
Repayment: Euro 0.4 million/year
Bank interest rate: 9 %
Duration of repayment: 17 years

## Slide 35: 11. Profitability Analysis
Chart: 
Chart: 
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Steuer | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 189597.3366 | 272802.5025 | 280306.7687 | 287613.6526 | 294712.9672
Figure xx: Taxes Vs years [own]
Taxes Vs Years:
Taxes Free: First 10 years
After 10 years: 30%

## Slide 36: 12. Results
NPV = Net Present Value, IRR = Internal Rate of Return, LEC = Levelized Cost of Energy, Min. DSCR = Minimum Debt Service Coverage Ratio, ADSCR = Average Debt Service Coverage Ratio
Positive NPV
Impressive IRR
Project promises cost efficiency and financial stability
Profitable project
 | Value | Unit
NPV | 303,893 (0.3 Million) | EUR
IRR | 8.730 | %
LEC | 0.0179 | EUR
Min. DSCR | 1.11 | 
ADSCR | 1.40 | 
Table xx: Financial result of wind farm [own]

## Slide 37: 14. Barriers and Obstacles
High bank tax rate
Land Use Conflicts
Maintenance Issues
Grid Integration
Limited Awareness
Preference for Solar Energy
Low energy price

## Slide 38: 6. Project Development Timeline
Study Laws and Regulations
12-20 months
12 -15 months
4-7 months
6-12 months
2-6 months
18 -30 months
6-12 months
3-6 months
Site Assessment
Land Leasing
Planning
Permitting
Financing
Constructions
Commissioning
From Greenfield to Operation:
Total timeline: 5 years – 9 years
Optimizing timeline: 3.5 years - 5 years

## Slide 39: 13. Vision for 2030/2050
Vision for 2030
Chart: 
| Other reneable sources | Wind Power
Sales | 360 | 140
Vision of India:
Achieve an installed renewable energy capacity: 500 GW
Wind energy production goal is 140 GW (28%)
Vision of Gujarat:
Achieve an installed renewable energy capacity: 128.6 GW
Increase the share of wind energy to 24%
Launch the first phase of offshore wind projects.
2024:
29.5 GW
2030:
128.6 GW
Figure xx: Vision of India renewable energy production for 2030 [own]
Figure xx: Vision of Gujarat renewable energy production for 2030 [own]

## Slide 40: 13. Vision for 2030/2050
Establish Gujarat as a global leader in wind energy.
Fully integrate smart grid solutions for efficient energy distribution.
Achieve a 50% reduction in carbon emissions from energy production.
Vision for 2050
Figure xx: Onshore wind turbine [https://sl.bing.net/hVlnu47HBZs]

## Slide 41: 13. Long Term Strategy
Improve Policy support
Advanced turbine technologies
Upgrade infrastructure
Encouraging community engagement
Spend more money in research and development of wind turbine
Energy storage system
Integrating smart grid
1
2
3
4
5
6
7

## Slide 42: 15. Conclusion
Location of Wind farm Perspective:
Advantage of Gujarat favourable policy environment
Manufacturing location of Suzlon company
Economic Perspective:
Reducing carbon emissions
Job creation
Local manufacturing
Profit Perspective:
Project Achieves a positive NPV
Impressive IRR

## Slide 43: 16. References