## Slide 1
Wind Farm Project Development, WiSe 2024/25
Team 3: Wind Farm Project in Gujarat, India
Presented by: Matriculation No.
Patil Rahul 750532
Mozafary Mostafa 750247
Soni Karan 760153
Guided by: M.Eng. Marina Blohm
Date : 15.01.2025
Place: Flensburg

## Slide 2: Agenda
1
Introduction
2
Legal Framework
3
Wind Farm Development
4
Environmental Impact and Conflicts
5
Land Leasing
6
Transportation
7
Economic Analysis
8
Barrier and Obstacles
9
Future Strategies

## Slide 3: 1. Introduction
India:
India ranks fourth in terms of installed wind power capacity
High Wind potential 132 GW with minimum 32% CUF
Ambitious Target(Wind) : 140 GW by 2030 (48 GW Current)
Energy Security
Figure 1.1: Information of renewable energy generation in India [38]

## Slide 4: 1. Introduction
Gujarat:
As May 2024, makes it the leading state in India for wind energy.
12.2 GW installed wind power capacity (26% Of total capacity)
Second rank, Tamil Nadu 11 GW
Why?
Geographic advantages
Government supports
Land policy
Tax benefits(First 10 Years no taxes)
Figure 1.2: Information of capacity wind potential in India [39]

## Slide 5: 2. Legal Framework
Gov.
Body
Ministry of New and Renewables (MNRE)
Central Agencies
National Institute of Wind Energy(NIWE)
State
Agencies
Gujarat Energy Development Agency(GEDA)
Ministry for Environment, forest and Climate change(MoEFCC)
Ministry of Defence (MoD)
Directorate General of Civil Aviation
Gujarat Power Corporation Limited (GPCL)
Gujarat Pollution Control Board(GPCB)
Revenue Department and Local Panchayat

## Slide 6: 2. Legal Framework
Consent to Establish from GSPCB
NOC from State Electricity board
Land Allotment letter
NOC from DLIR Department
Permission for Forest Department
NOC from Mining Department
NOC from AAI and MoD
Power Purchase Agreement
NOC from Village Panchayat
Permits and approvals:

## Slide 7: 2. Legal Framework
Criteria | Buffer Distance
Micro siting within Wind Farm | 2D-3D
Public Roads, railway tracks, highways, buildings, public institutions | HH+0.5∙RD+5m
Eco-Sensitives Zones | 10 KM
Forest | 6.6 M from Ground (Power Lines)
Satic Air Defence Radar | 10 KM
Airports and Airstrips | 20 KM
Rivers | 250 M
Micro siting guidelines:
Table 2.1: Information of micro siting guidelines [7]

## Slide 8: 3. Wind Farm Development
Identification of potential site
Pre-feasibility study
Grid connectivity
Land acquisition and approvals
Environmental and social impact assessment
Financial planning
Wind farm development

## Slide 9: 3. Wind Farm Development
Identification of Potential Sites (QGIS)
Analyse Wind site:
Wind speed data at 100m height
Coordinate Reference System: WGS 84/ UTM zone 43N, Authority ID: EPSG:32643
GIS Layers | Distances [m]
Buildings | 250
Forests | 10,000
Military Areas | 10,000
Railways/ Industrial | 250
Roads | 250
Airports/ Airfields | 20,000
Rivers | 250
Figure 3.1: White map area [own]
Table 3.1: GIS layers information [own]
Integrated wind speed data onto the white map layer [Use the clip Raster by Mask Layer Tool]

## Slide 10: 3. Wind Farm development
Pre-Feasibility study
Criteria For site selection
b
Wind Resource Availability
Topography and Terrain
Land Availability
Grid Infrastructure
Environmental considerations
Soil Conditions
Logistics

## Slide 11: 3. Wind Farm development
Selection of site
Figure 3.3: Wind farm location [own]
Figure 3.2: White map area [own]

## Slide 12: 3. Wind Farm development
Used Google Earth Pro for a comprehensive site assessment
Figure 3.4: Poladia wind farm [own]
Figure 3.5: Poladia wind farm[own]
Site selection

## Slide 13: 3. Wind Farm Development
Type of Land and Soil Condition
Soil :- Residual soil with reddish brown in color
Land :- Private farmland (100 X 100 m)
Site selection
Figure 3.6: Poladia wind farm [own]

## Slide 14: 3. Wind Farm Development
Elevation Profile of Site
Site selection
Figure 3.7: Poladia wind farm [own]

## Slide 15: 3. Wind Farm Development
Six Suzlon 2.1 MW wind turbines, strategically positioning them to account for wind direction
Predominant Wind direction of Site
Figure 3.8: Poladia wind farm [own]
Figure 3.9: Wind rose [40]

## Slide 16: 3. Wind Farm Development
Wind Farm Capacity :- 12.6 MW
Turbine:- S97*2100(112 m HH)
Why Suzlon?
Local Manufacturer
High-capacity utilization factor (CUF)
Low Cost Availability
Logistics
Selection of WTGs
Figure 3.10: SUZLON wind turbine [41]

## Slide 17: 3. Wind Farm Development
Our wind farm has a capacity of 12.6 MW, which is relatively below 20 MW. Therefore, we utilized an available substation.
The substation, named Renew Wind Energy (AP2) Pvt Ltd, operates at 33/220 kV.
The length of the 33 kV line from the inside wind farm is 4.41 Km and from wind farm area to the pooling substation is 16 km.
Followed existing roads for transmission line in order to avoid conflicts and permissions.
Grid infrastructure and cable routing
Figure 3.11: Grid infrastructure and cable routing [own]

## Slide 18: 4. Environment Impact and Conflicts
Environmental Conflicts in Wind Energy Projects
Land Use Challenges:
Competition over agricultural, forest, and community lands.
Protected areas like the Western Ghats face ecological damage.
Biodiversity Impact:
Bird and bat fatalities due to turbine collisions.
Habitat destruction from road construction and deforestation.
Environmental Trade-offs:
Noise pollution and shadow flicker disturb local communities.
Changes in local hydrology and microclimates from large-scale projects.
Figure 4.1 [41]

## Slide 19: 4. Environment Impact and Conflicts
Socio-Economic and Governance Conflicts:
Community Livelihood Loss:
Displacement from common lands and inadequate compensation.
Encroachment on tribal lands and loss of natural resources.
Regulatory Gaps:
Lack of stringent Environmental Impact Assessments (EIA).
Unplanned projects ignore landscape-scale implications.
Competing Priorities:
Conflict between energy development and agricultural or tourism needs.
Balancing renewable energy goals with environmental preservation.
Figure 4.2 [42]

## Slide 20: 4. Environment Impact and Conflicts
Benefits of the Wind Park Project
Job Creation:
  1 full-time site manager
  2 full-time operators for maintenance and repairs
Profit for Landowners
Addressing Power Outages:
  A reliable electricity supply for the village (currently interruptions caused by infrastructure issues, scheduled cuts, or weather conditions.)
Infrastructure Development:
  Supports the expansion of rural infrastructure
Strategies of community engagement
Figure 4.3 [43]

## Slide 21: 4. Environment Impact and Conflicts
Community Meeting
Engage Local Leaders
Transparency
Benefit Sharing
Regular Updates
Community Feedback
Raise Awareness
Long Term Engagement
Community Meetings: Highlight benefits (jobs, infrastructure, clean energy) and address concerns.
Engage Local Leaders: Gain trust and support from key influencers.
Transparency: Share project details, timelines, and impacts openly.
Benefit Sharing: Provide scholarships, infrastructure upgrades, or community funds.
Regular Updates: Keep everyone informed on progress through consistent communication.
Strategies of community engagement

## Slide 22: 5. Land Leasing
Land Leasing Overview:
Secure land for wind park projects under Gujarat’s progressive renewable energy policies.
Lease Duration: 40 years for government fallow land.
Policy Scope: Focus on renewable energy generation to support Gujarat’s industrial and green energy goals.
Eligibility: Companies with experience in renewable energy and sufficient financial capacity.
Figure 5.1 [44]

## Slide 23: 5. Land Leasing
Eligibility and Allocation:
Eligibility:
Minimum 500 MW renewable energy generation experience.
Net worth: ₹1200 crore/lakh metric tons of energy/year.
Industries requiring 1 lakh metric tons/year of green hydrogen prioritized.
Land Allocation:
Exclusive use for wind energy projects.
Cap of 30 lakh metric tons/year green hydrogen production per entity.
Reserved land for future state requirements.
Figure 5.2 [45]

## Slide 24: 5. Land Leasing
Application and Approval Process:
Application Submission:
Preliminary preparation report (technical and financial).
Verification:
Nodal Agency (GPCL) validates eligibility and technical aspects.
Review & Recommendation:
High Power Committee (HPC) evaluates proposals.
Final Approval:
Government decision via Revenue Department.
Lease agreement executed with a tripartite agreement.
Figure 5.3 [46]

## Slide 25: 5. Land Leasing
Responsibilities & Compliance:
Developer Responsibilities:
Infrastructure: Roads, transmission, and water systems.
Financial: ₹180,000 (€ 2050)/ha annual rent (15% increase every 3 years).
Progress Milestones:
  50% capacity in 3 years.
  100% capacity in 8 years.
Compliance:
Periodic reviews to ensure milestones.
Unused land subject to reclamation.
Figure 5.4: [48]

## Slide 26: 5. Land Leasing
Number of owner | Area ( ) | Financial by rule (1/year) | Bonus (1/year) | Total (per year)
1 (WTG) |  | € 2050 | € 921 | € 2971
2 (WTG) |  | € 2050 | € 921 | € 2971
3 (WTG) |  | € 2050 | € 921 | € 2971
4 (WTG) |  | € 2050 | € 921 | € 2971
5 (WTG) |  | € 2050 | € 921 | € 2971
6 (WTG) |  | € 2050 | € 921 | € 2971
7 (transmission line) |  | € 4100 | € 921 | € 2971
Number of owner |  | Financial by rule (1/year) | Bonus (1/year) | Total (per year)
1 (WTG) |  | € 2050 | € 921 | € 2971
2 (WTG) |  | € 2050 | € 921 | € 2971
3 (WTG) |  | € 2050 | € 921 | € 2971
4 (WTG) |  | € 2050 | € 921 | € 2971
5 (WTG) |  | € 2050 | € 921 | € 2971
6 (WTG) |  | € 2050 | € 921 | € 2971
7 (transmission line) |  | € 4100 | € 921 | € 2971
Table 5.1: Land leasing own strategy [own]
Bonus
Land Leasing strategy
Figure 5.5: Information of landowner [own]

## Slide 27: 6. Transportation
NH48
NH4
NE1
NH64
NH27
754k
1
2
3
4
Wind Turbine Manufacturing components | Manufacturing Locations | Distance between Manufacturing location to Wind farm [km]
Nacelle | Daman, Gujarat, India | 743
Nacelle Cover | Daman, Gujarat, India | 743
Hub | Daman, Gujarat, India | 743
Rotor Blades | Bhuj, Gujarat, India | 57
Tower | Gandhidham, Gujarat, India | 136
Electrical | Vadodara, India | 544
Location: Poladia, Gujarat, India

## Slide 28: 6. Transportation
Distance Between State highway to Wind Farm: 25 km
Time Duration :- 3 to 4 Hours

## Slide 29: 7. Economic Analysis
Input Parameters of Annual Energy For Wind Farm:
Figure 7.1: Wind pro report [own]
Figure 7.2: Wind pro report [own]

## Slide 30: 7. Economic Analysis
Input Parameters to calculate Profit analysis calculation:
Parameter | Economics | Unit
Number of WT | 6 | -
Installation output | 2100 | KW
Total output | 12600 | kW
Gross Energy Yield | 39924500 | KWh/a
Total losses | 2.20 | %
Net Energy Yield | 399,046,161 | kWh
Site Quality | 71.04 | %
Feed in Tariff | 0.033 | Euro/kWh
Total Investment Costs | 98,07,253 | Euro
Total Operating Costs | 1,05,000 | Euro
Constant Payment Loan Type (Debt ratio) | 72.73 | %
Equity | 26,74,327 | Euro
Term | 17 | Years
Interest rate of Bank | 9.0 | %
Debt Capital | 71,32,926 | Euro
Inflation rate | 5.16 | %
Table 7.1: Input parameters for calculating profit analysis [own]
Take data from WindPro Calculation
INR 3 per kwh
Capital costs:
1 MW = INR 70 million (Euro 0.791 million)
Operating costs:
1 MW = INR 0.75 million/year = (Euro 0.105 million)
Last 10 years average

## Slide 31: 7. Economic Analysis
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044
Income | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158
Figure 7.3: Income Vs Years [own]
Income vs Years:
Income: 1.29 Million/ year
operation period: 20 years

## Slide 32: 7. Economic Analysis
Chart: Operating costs
Chart: 
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Betriebskosten | 260419.05 | 266117.7772 | 272110.6157 | 128412.7445 | 135040.1263 | 142009.5472 | 149338.6599 | 157046.0282 | 165151.1737 | 173674.6257 | 182637.9732 | 192063.919 | 201976.3378 | 212400.3366 | 223362.318 | 234890.0472 | 247012.7226 | 259761.0492 | 273167.3169 | 287265.4822
Figure 7.4: Operating cost Vs Years [own]
Operating costs vs Years:
Operating costs: 0.25 Million staring year
operation period: 20 years

## Slide 33: 7. Economic Analysis
Chart: 
| Eigenkapital | Fremdkapital
 | 0.2727 | 0.7273
Chart: Duration in years
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Repayment | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581
Interest | 641963.3029 | 641963.3029 | 641963.3029 | 623082.0293 | 585319.4821 | 547556.9349 | 509794.3876 | 472031.8404 | 434269.2932 | 396506.7459 | 358744.1987 | 320981.6515 | 283219.1042 | 245456.557 | 207694.0098 | 169931.4625 | 132168.9153 | 94406.3681 | 56643.8208 | 18881.2736
Figure 7.5: Investment [own]
Figure 7.6: Debt service Vs years [own]
Debt service Vs Years:
Repayment: Euro 0.4 million/year
Bank interest rate: 9 %
Duration of repayment: 17 years

## Slide 34: 7. Economic Analysis
Chart: 
Chart: 
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Steuer | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 189597.3366 | 272802.5025 | 280306.7687 | 287613.6526 | 294712.9672
Figure 7.7: Taxes Vs years [own]
Taxes Vs Years:
Taxes Free: First 10 years
After 10 years: 30%

## Slide 35: 7. Economic Analysis
NPV = Net Present Value, IRR = Internal Rate of Return, LEC = Levelized Cost of Energy, Min. DSCR = Minimum Debt Service Coverage Ratio, ADSCR = Average Debt Service Coverage Ratio
Positive NPV
Impressive IRR
Project promises cost efficiency and financial stability
Profitable project
 | Value | Unit
NPV | 303,893 (0.3 Million) | EUR
IRR | 8.730 | %
LEC | 0.0179 | EUR
Min. DSCR | 1.11 | 
ADSCR | 1.40 | 
Table 7.2: Financial result of wind farm [own]

## Slide 36: 8. Barriers and Obstacles
High bank tax rate
Land Use Conflicts
Maintenance Issues
Grid Integration
Limited Awareness
Preference for Solar Energy
Low energy price

## Slide 37: 9. Project Development Timeline
Study Laws and Regulations
12-20 months
12 -15 months
4-7 months
6-12 months
2-6 months
18 -30 months
6-12 months
3-6 months
Site Assessment
Land Leasing
Planning
Permitting
Financing
Constructions
Commissioning
From Greenfield to Operation:
Total timeline: 5 years – 9 years
Optimizing timeline: 3.5 years - 5 years

## Slide 38: 10. Future Strategy
Vision for 2030
Chart: 
| Other reneable sources | Wind Power
Sales | 360 | 140
Vision of India:
Achieve an installed renewable energy capacity: 500 GW
Wind energy production goal is 140 GW (28%)
Vision of Gujarat:
Achieve an installed renewable energy capacity: 128.6 GW
Increase the share of wind energy to 24%
Launch the first phase of offshore wind projects.
2024:
29.5 GW
2030:
128.6 GW
Figure 10.1: Vision of India renewable energy production for 2030 [own]
Figure 10.2: Vision of Gujarat renewable energy production for 2030 [own]

## Slide 39: 10. Future Strategy
Establish Gujarat as a global leader in wind energy.
Fully integrate smart grid solutions for efficient energy distribution.
Achieve a 50% reduction in carbon emissions from energy production.
Vision for 2050
Figure 10.3: Onshore wind turbine [47]

## Slide 40: 10. Future Strategy
Improve Policy support
Advanced turbine technologies
Upgrade infrastructure
Encouraging community engagement
Spend more money in research and development of wind turbine
Energy storage system
Integrating smart grid
1
2
3
4
5
6
7

## Slide 41: 11. References
[1] “MINISTRY OF NEW AND RENEWABLE ENERGY,” 01 2024. [Online]. Available: https://mnre.gov.in/wind-overview. [Accessed 2024 10 02].
[2] “A Deep Dive into Wind Energy Farms in India: Tapping into the Power of the Breeze,” Green Energy, 23 01 2024. [Online]. Available: https://powerefficiency.com/wind-energy-farms-in-india/. [Accessed 02 10 2024].
[3] “gujarat-bags-award-for-highest-wind-power-installed-capacity,” thehindubusinessline, 15 06 2024. [Online]. Available: https://www.thehindubusinessline.com. [Accessed 2 10 2024].
[4] A. P. Z. P. C. Draxl, “Wind Resource Assessment,” NREL National Renewable Energy Laboratory, July, 2014.
[5] M. Gupta, “Scaling Challenges In Gujarat: Adani’s 300 MW Wind Farm Project And Its Journey Through Regulatory And Logistical Hurdles,” WINDINSIDER EMPOWERING THE WIND SECTOR, 13 05 2024. [Online]. Available: https://windinsider.com. [Accessed 10 10 2024].
[6] Suzlon Group, “Suzlon secures a repeat order of 193.2 MW from The KP Group in Gujarat,” 21 December 2023. [Online]. Available: https://www.suzlon.com. [Accessed 13 10 2024].
[7] MINISTRY OF NEW AND RENEWABLE ENERGY, “Clarification to the ‘Guidelines for Development of Onshore Wind Power Projects’ and amendments,” Government of India, 18 12 2024. [Online]. Available: https://mnre.gov.in/en/document/clarification-to-the-guidelines-for-development-of-onshore-wind-power-projects-and-amendments/. [Accessed 15 11 2024].
[8] thc.nic.in, “THE HAZARDOUS WASTES (MANAGEHANDLING AND TRANSBOUNDARY MOVEMENT) RULES, 2008,” Official Gazeette, MARCH, 2010.
[9] Forest Clearance, “Forest Conservation Rules,” 2003. [Online]. Available: https://forestsclearance.nic.in. [Accessed 17.11.2024].
[10] National Board for Wildlife, Ministry of Environment and Forest, India, “Guidelines for linear infrastructure intrusions in natural areas: roads and powerlines,” 10 Octomber 2011. [Online]. Available: https://moef.gov.in. [Accessed 25 11 2024].
[11] India Air Force, “GUIDELINES FOR ISSUE OF NOC FOR CONSTRUCTIONS AROUND INDIAN AIR FORCE AERODROMES,” 12 2021. [Online]. Available: https://indianairforce.nic.in. [Accessed 11 11 2024].
[12] DTU, “GLOBAL WIND ATLAS,” DTU, ESMAP, WORLD BANK GROUP, VORTEX, [Online]. Available: https://globalwindatlas.info. [Accessed 24 11 2024].

## Slide 42: 11. References
[13] GEOFABRIK, “OpenStreetMap Data Extracts,” [Online]. Available: https://download.geofabrik.de/. [Accessed 25 11 2024].
[14] Openinframap, [Online]. Available: openinframap.org. [Accessed 26 12 2024].
[15] Government of Gujarat, “Policy-2023 for leasing the government fallow land for green hydrogen production using non-conventional energy sources such as solar, wind, wind solar hybrid energy.,” 08 May 2023. [Online]. Available: https://www.eqmagpro.com. [Accessed 13 10 2024].
[16] ARCADIS India Pvt. Ltd., “ENVIRONMENTAL & SOCIAL IMPACT ASSESSMENT: 250 MW Wind Power Project in Kutch district, Gujarat,” ARCADIS, Kutch, 2017.
[17] Gujarat Goverment , “policy_files,” 2016. [Online]. Available: https://geda.gujarat.gov.in. [Accessed 28 11 2024].
[18] suzlon, “supply-chain-management-and-manufacturing,” 2024. [Online]. Available: https://www.suzlon.com. [Accessed 12 12 2024].
[19] A. Joshi, “Gujarat Sets ₹2.84/kWh Tariff for wind projects below 10 MW comnnissioned by 2027,” MERCOM Clean Energy Insights, 04 09 2024. [Online]. Available: https://www.mercomindia.com. [Accessed 25 12 2024].
[20] Macrotrends, “India Inflation Rate 1960-2024,” Macrotrends LLC, [Online]. Available: https://www.macrotrends.net. [Accessed 25 12 2024].
[21] U. Ehlers, Project financing in the wind power sector (Lecture Note), Flensburg, Germany: Hochschule Flensburg Prof. Marina Blohm, 20.11.2024.
[22] EI News Network, “GERC Updates Regulations for Small Wind Projects,” energetica INDIA, 05 September 2024. [Online]. Available: https://www.energetica-india.net. [Accessed 27 12 2024].
[23] iNDEXTb/GM(Project&Tech.), “Wind Farm - An Opportunity for Investment in Gujarat,” Goverment of Gujarat, Gandhinagar.
[24] M. B. Arshi Banu P S, “Wind energy feasibility and wind turbine selection studies for the city Surat, India,” Clean Energy, vol. 8, no. 3, pp. 166-173, 2024.
[25] L. C. a. A. B. Vaisakh Suresh Kumar, “Scaling up small wind turbines in India (Barriers and options for the way forward),” WRI-INDIA.ORG and CLEAN , Delhi, 2024.
[26] A. P. a. Z. P. . Draxl, “Wind Resource Assessment,” National Renewable Energy Laboratory (NREL), 2014.
[27] R. m. https://www.mercomindia.com/gujarat-land-policy-solar-wind-projects, “Gujarat's New Land Policy for Solar, Wind Projects to Make Developers More Accountable,” MERCOM, Clean Energy Insights, 17 September 2020. [Online]. Available: https://www.mercomindia.com/gujarat-land-policy-solar-wind-projects. [Accessed 05 10 2024].

## Slide 43: 11. References
[28] D. M. Blohm, Lecture Notes on Wind Farm Development, Flensburg, 2024.
[29] EU-INDIA CLEAN ENERGY & CLIMATE PARTNERSHIP, “About the partnership,” European Union , 30 March 2016. [Online]. Available: https://www.cecp-eu.in. [Accessed 13 10 2024].
[30] Nature India, “Is the drive for clean energy throwing environmental caution to the wind?,” NEWS FEATURE, 16 June 2019.
[31] P. C. Abhishek Gawande, “Environmental and social impacts of wind energy: a view point with reference to India,” Indian Institute of Forest Management, Bhopa, 2019.
[32] Gujarat Urja Vikas Nigam Ltd, “REQUEST FOR SELECTION (RfS),” 10 07 2023. [Online]. Available: https://jmkresearch.com. [Accessed 20 10 2024].
[33] V. Shah, “India Sets Sail on 1 GW Offshore Wind Energy Projects in Gujarat, Tamil Nadu,” goodreturns, 19 June 2024. [Online]. Available: https://www.goodreturns.in. [Accessed 22 10 2024].
[34] Editorial Team, “Gujarat: Pioneering Sustainable Wind Power Generation in India,” SSMB.IN, 19 September 2024. [Online]. Available: https://ssmb.in/2024/09/19/gujarat-pioneering-sustainable-wind-power-generation-in-india/. [Accessed 22 10 2024].
[35] GE VERNOVA, “GE acquires 49% stake in Continuum onshore wind farm in support of the energy transition in India,” GE, [Online]. Available: https://www.gevernova.com. [Accessed 22 10 2024].
[36] Gujarat Energy Development Agency, Gujarat Government, [Online]. Available: https://geda.gujarat.gov.in. [Accessed 22 10 2024].
[37] Wind farm BoP, “Wind farm testing and commissioning,” 2017, [Online]. Available: https://www.windfarmbop.com/. [Accessed 22 10 2024].
[38] India Renewable energy race :- https://www.downtoearth.org.in/renewable-energy/india-s-renewable-energy-race-mp-up-will-take-more-than-50-years-to-meet-2022-target-at-current-pace-85195, 10/01/2025
[39] India Wind Potential, https://www.tandfonline.com/doi/full/10.1080/15435075.2021.1978447, 10/01/2025.
[40] https://www.indianclimate.com/show-data.php?request=CRBLWINFEW
[41] https://www.netsolwater.com/what-is-major-environmental-conflicts-in-india-with-example.php?blog=130
[42] https://www.sciencedirect.com/science/article/pii/S2214629621004357

## Slide 44: 11. References
[43] the world's biggest blackout, 31th July 2012 [source:nbcnews]
[44] https://www.crematrix.com/blog/what-are-the-different-types-of-commercial-leases-in-india
[45] Eligibility | Senior Services of Illinois
[46] Approval Process - Free of Charge Creative Commons Post it Note image
[47] https://sl.bing.net/hVlnu47HBZs
[48] What are the 4 Types of CSR - Corporate Social Responsibility? - India CSR
What to know more about project?
Check out our GitHub 