## Slide 1
Wind Farm Project Development, WiSe 2024/25
Team 3: Wind Farm Project in Gujarat, India
Presented by: Matriculation No.
Mozafary Mostafa 750247
Patil Rahul 750532
Soni Karan 760153
Guided by: Prof. Marina Blohm
Date : 15.01.2025
Place: Flensburg

## Slide 2: Overview
Overview of wind farm development in Gujarat
Guidelines and Regulations
Project development timeline
Wind Area selection
Grid infrastructure and cable routing
Strategies community engagement
Land Leasing
Addressing conflicting Interests
10. Logistics and Transformation
11. Profitability Analysis
12. Results
13. Long Term Strategy
14. Barriers and Obstacles
15. Conclusion
16. References

## Slide 3: 1. Overview of Wind Farm Development in Gujarat
India:
India ranks fourth in terms of installed wind power capacity.
Several Large Wind Farm: Tamil Nadu, Gujarat, Maharashtra.
Gujarat:
As May 2024, makes it the leading state in India for wind energy.
11,823 MW installed wind power capacity
Second rank, Tamil Nadu 10,743 MW
Why?
Geographic advantages, Government supports, Land policy, Tax benefits.

## Slide 4: 2. Methodology

## Slide 5: 3. Guidelines and Regulations
Guidelines for micro siting of wind turbine:
Maintain a distance of (D-Rotor Diameter) distance perpendicular to the predominant wind direction and distance in the predominant wind direction
Maintain a distance of (Hub Height+ Half Rotor Diameter +5 meters) from Public Roads, railway tracks, highways, buildings, public institutions and EHV lines
Application for Hazardous Waste (Grease, Coolant oil and Lubricating oil) Authorisation
Permission for forest department
Eco-Sensitive zones (wildlife sanctuaries)
NOC from Airport authority of India and Ministry of defence

## Slide 6: 4. Wind Area Selection
Analyse Wind Farm:
Wind speed data at 100m height
Coordinate Reference System: WGS 84/ UTM zone 43N, Authority ID: EPSG:32643
Integrated wind speed data onto the white map layer [Use the clip Raster by Mask Layer Tool]
GIS Layers | Distances [m]
Buildings | 250
Forests | 10,000
Military Areas | 10,000
Railways/ Industrial | 250
Roads | 250
Airports/ Airfields | 20,000
Rivers | 250

## Slide 7: 4. Wind Area Selection
Used Google Earth Pro for a comprehensive site assessment

## Slide 8: 4. Wind Area Selection
Six Suzlon 2.1 MW wind turbines, strategically positioning them to account for wind direction

## Slide 9: 5. Grid Infrastructure and Cable Routing
Our wind farm has a capacity of 12.6 MW, which is relatively below 20 MW. Therefore, we utilized an available substation.
The substation, named Renew Wind Energy (AP2) Pvt Ltd, operates at 33/220 kV.
The length of the 33 kV line from the wind farm area to the pooling substation is 20 km.

## Slide 10: 6. Project Development Timeline

## Slide 11: 7. Strategies of Community Engagement
Community Meeting
Engage Local Leaders
Transparency
Benefit Sharing
Regular Updates
Community Feedback
Raise Awareness
Long Term Engagement

## Slide 12: 8. Land Leasing
Private:
Land Lease period: Max. 40 years
Annual rent: ₹15,000 (€ 150 – €170) per area, subject to a 15% increase every three years
Approval Process:
Step 1: Title clearance
Step 2: Agreement to Sell (ATS) and Sale Deed
Step 3: Application and Obtaining 89A Permission from revenue department
Step 4: Conversion to Old Tenure Land & Payment of Premium
Step 5: Apply and Obtain 65 Kh Permission (Non-Agricultural or NA Use)

## Slide 13: 9. Addressing Conflicting Interests

## Slide 14: 10. Logistics and Transformation
NH48
NH4
NE1
NH64
NH27
754k
1
2
3
4
Wind Turbine Manufacturing components | Manufacturing Locations | Distance between Manufacturing location to Wind farm [km]
Nacelle | Daman, Gujarat, India | 743
Nacelle Cover | Daman, Gujarat, India | 743
Hub | Daman, Gujarat, India | 743
Rotor Blades | Bhuj, Gujarat, India | 57
Tower | Gandhidham, Gujarat, India | 136
Electrical | Vadodara, India | 544
Location: Poladia, Gujarat, India
Why Suzlon company wind turbine?
Manufacturing in Gujarat
Government provides incentives (Made in India)

## Slide 15: 10. Logistics and Transformation
Distance Between State highway to Wind Farm: 25 km

## Slide 16: 11. Profitability Analysis
Input Parameters to calculate Profit analysis calculation:

## Slide 17: 11. Profitability Analysis
Input Parameters to calculate Profit analysis calculation:
Parameter | Economics | Unit
Number of WT | 6 | -
Installation output | 2100 | KW
Total output | 12600 | kW
Gross Energy Yield | 39026700 | KWh/a
Total losses | 2.20 | %
Net Energy Yield | 3,81,68,113 | kWh
Site Quality | 71.04 | %
Feed in Tariff | 0.033 | Euro/kWh
Total Investment Costs | 98,07,253 | Euro
Total Operating Costs | 1,05,000 | Euro
Constant Payment Loan Type (Debt ratio) | 72.73 | %
Equity | 26,74,327 | Euro
Term | 17 | Years
Interest rate of Bank | 9.0 | %
Debt Capital | 71,32,926 | Euro
Inflation rate | 5.16 | %

## Slide 18: 11. Profitability Analysis
Chart: Operating costs
Chart: 
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044
Income | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158 | 1259547.7158
Chart: Operating costs
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Betriebskosten | 260419.05 | 266117.7772 | 272110.6157 | 128412.7445 | 135040.1263 | 142009.5472 | 149338.6599 | 157046.0282 | 165151.1737 | 173674.6257 | 182637.9732 | 192063.919 | 201976.3378 | 212400.3366 | 223362.318 | 234890.0472 | 247012.7226 | 259761.0492 | 273167.3169 | 287265.4822

## Slide 19: 11. Profitability Analysis
Chart: 
| Eigenkapital | Fremdkapital
 | 0.2727 | 0.7273
Chart: Debt service installment loan
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Repayment | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581 | 419583.8581
Interest | 641963.3029 | 641963.3029 | 641963.3029 | 623082.0293 | 585319.4821 | 547556.9349 | 509794.3876 | 472031.8404 | 434269.2932 | 396506.7459 | 358744.1987 | 320981.6515 | 283219.1042 | 245456.557 | 207694.0098 | 169931.4625 | 132168.9153 | 94406.3681 | 56643.8208 | 18881.2736

## Slide 20: 11. Profitability Analysis
Chart: 
Chart: Taxes
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
Steuer | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 50514.47 | 264109.8234 | 271614.0896 | 278920.9734 | 286020.288

## Slide 21: 12. Results
NPV = Net Present Value, IRR = Internal Rate of Return, LEC = Levelized Cost of Energy, Min. DSCR = Minimum Debt Service Coverage Ratio, ADSCR = Average Debt Service Coverage Ratio
Positive NPV
Impressive IRR
Project promises cost efficiency and financial stability
Highly profitable project
 | Value | Unit
NPV | 58,192 | EUR
NPV costs | 25,42,246 | EUR
NPV kWh | 39,56,79,974 | EUR
IRR | 7.557 | %
LEC | 0.0184 | EUR
Min. DSCR | 1.08 | 
ADSCR | 1.38 | 

## Slide 22: 13. Long Term Strategy
Vision and Goals:
By 2030:
Achieve an installed wind energy capacity of 15 GW.
Increase the share of wind energy to 20% of the state's total energy mix.
Launch the first phase of offshore wind projects.
By 2050:
Establish Gujarat as a global leader in wind energy.
Fully integrate smart grid solutions for efficient energy distribution.
Achieve a 50% reduction in carbon emissions from energy production.
Strategy to achieve goal:
Improve Policy support
Advanced turbine technologies
Upgrade infrastructure
Integrating smart grid
Encouraging community engagement
Spend more money in research and development of wind turbine
Energy storage system

## Slide 23: 14. Barriers and Obstacles
High Initial Costs
Land Use Conflicts
Environmental Concerns
Maintenance Issues
Grid Integration
Standardization and Quality Control
Limited Awareness
Preference for Solar Energy

## Slide 24: 15. Conclusion
Location of Wind farm Perspective:
Taking advantage of Gujarat favourable policy environment
Manufacturing location of Suzlon company
Economic Perspective:
Reducing carbon emissions
Job creation
Local manufacturing
Project faces significant challenges:
high bank tax rates
low energy prices
which reduce its overall profitability.
Suggestions:
Increasing capital investment
Raising energy prices or seeking government support for loans
Profit Perspective:
Project Achieves a positive NPV
Impressive IRR

## Slide 25: 16. References